## Slide 1: Introduction to IP Multicast
<Chapters 1 - 3 in Textbook>
Seok J. Koh

## Slide 2: Table of Contents
Internet Multicasting Overview
Taxonomy: Broadcast, Multicast and Unicast
Why Multicast ?
IP addressing Overview
Subnet Broadcasting
Multicast IP over LAN (Subnet)

## Slide 3: Internet Multicasting
Multicast Applications
  One-to-Many
  Many-to-Many
Session (Group) Management
  Multicast Session Announcement
    Multicast Address & Port Number
    Session-specific Information
    Authentication/Security
  Session Registration/Enrollment
Multicast Routing Protocols
  Multicast Forwarding
Reliable Multicast Transport
  End-to-end Reliable Delivery of Data

## Slide 4: Multicast Applications (1)
One-to-Many
  File Dissemination
  Software Upgrade/Simulations
  Internet Broadcasting
  Real-time Financial Data Distribution, etc
Many-to-Many
  Group Conferencing
  Whiteboard applications, etc
Other types ?
  Remote Education: with Unicast feedback channels

## Slide 5: Multicast Applications (2)
Classifications & Characteristics ?
  Application Types, Latency Requirements, Session Duration, Group Size (Scalability), Geographical Scope of the Group, Time-sensitiveness, etc
  An Example of Classification

## Slide 6: Session Management
Session Creation
  SDP(Session Description Protocol):RFC 2327
    Session-Specific Information
Session Announcement
  SAP(Session Announcement Protocol): Draft
    224.2.127.254 or 224.2.128 (SAPv1)
  SIP(Session Initiation Protocol): RFC2543
  HTTP: Web Page
  SMTP: E-mail
Session Registration
  Authentication/Security
  Business Perspective: Billing & Charging
  Application-Specific or general Group Management?

## Slide 7: Multicast Routing & Forwarding (1)
Multicast Tree Construction
  Connecting Sender(s) to Receivers
  With help of Multicast Routing Protocols
  Network Layer Tree (Between Routers)
    An Input Interface for a Group
    Output Interfaces for a group
  Data Forwarding Path
Source

## Slide 8: Multicast Routing & Forwarding (2)
History in terms of RFCs
  Class D address: 1985
  Steve Deering (Stanford) Ph. D thesis
    RFC 966 (1985), RFC 988 (1986)
    RFC 1112 (1988): IGMPv1
      Host Extensions for IP Multicasting
  DVMRP: RFC 1075 (1988)
  MOSPF: RFC 1585 (1994)
  CBT: RFC 2189 & RFC 2201 (1997)
  IGMPv2: RFC 2236 (1997)
  PIM-SM: RFC 2362 (1998)
  The Others

## Slide 9: Multicast Routing & Forwarding (3)
Overview of Multicast Routing Architecture

## Slide 10: Reliable Multicast Transport (1)
Reliable Delivery
  Error Recovery by Retransmissions of Lost packets
  Flow and Congestion Control: Data Transmission
TCP in unicast
  Sliding Window, ACK & retransmissions
  Linear Increase & Exponential Back-off: Data Rate
Reliability Issues in Multicast Transport
  Scalability in Error Control
    ACK/NACK implosion
  Congestion Control (for ISP)
    RTT estimation
    Slow Receivers
  Security: Secure Multicast,Key Distribution

## Slide 11: Reliable Multicast Transport (2)

## Slide 12: Reliable Multicast Transport (3)
IRTF/RMRG(Reliable Multicast Research Group)
  So many research works
IETF RMT WG: 1999. 3
  “One Size doesn’t fit all”
  BB(Building Blocks)
    Congestion Control
    Generic Router Assist
    Forward Error Correction, etc
  PI(Protocol Instances)
    TRACK:Tree based ACK
    NORM: NACK Oriented Reliable Multicast
    FEC based ALC (Asynchronous Layered Coding)

## Slide 13: Reliable Multicast Transport (4)
Example: TRACK (Tree based ACK)

## Slide 14: Related IETF Working Groups
Transport Area
  RMT (Reliable Multicast Transport)
  MALLOC (Multicast Address Allocation)
  MMUSIC (Multiparty Multimedia Session Control)
Routing Area
  IDMR (Inter-Domain Multicast Routing)
  MOSPF (Multicast Extensions to OSPF)
  PIM (Protocol Independent Multicast)
  MSDP (Multicast Source Discovery Protocol)
  BGMP (Border Gateway Multicast Protocol)
  SSM (Source Specific Multicast)
Operations & Management Area
  MBONED (MBONE Deployment)

## Slide 15: New Trends for IP Multicast
SSM (Source Specific Multicast) Routing
  Intra-Domain
  with help of IGMP version 3
  Scalable and Easy to Deploy: ?
Application-Level Multicast (Application-Relay)
  Unicast : from Sender to a Local Area
  Multicast : Multicast within each Local Area
SGM (Small Group Multicast)
  Small Group: How Many ?, 10 - 50 ?
  IP Packet contains the list of Receivers
BGMP (Border Gateway Multicast Protocol)
  Inter-Domain
  A Long-Term Solution: ?

## Slide 16: Taxonomy
Unicast: One-to-One
Broadcast: One-to-All
  Limited broadcast
  Subnet-specific broadcast
  All-subnets broadcast
Multicast:
  One to Many: Uni-directional
  Many to Many: Bi-directional
Anycast (in IPv6): One to Nearest
  Neighborhood (e.g. Router or DNS) Discovery

## Slide 17: Broadcast
Source
R
R

## Slide 18: Multicast
Source
R
R

## Slide 19: Replicated Unicast
Source
R
R

## Slide 20: Need for Multicast (1)
“Efficiency”
  Broadcast with broadcast address
  Replicated Unicast: N unicast
  Network Layer Multicast
Broadcast
  Loop between Subnets
    Broadcast Storm
  Un-interested Hosts: simply receive & discard
    Bandwidth Waste in the network
    CPU degradation in the hosts

## Slide 21: Need for Multicast (2)
Replicated Unicast
  Source must keep track of the network addresses for all receivers (management overhead)
  Latency (gap) across the group: during the N unicasts
  Traffic burden at near source
Network-Layer Multicast
  Only one copy per a link
  Only the interested receivers (via IGMP)
  Senders need not know the group members

## Slide 22: Need for Multicast (3)
Another:
  Application Level Multicast (e.g. PointCast)
    Sender (server) - Relay (dedicated server): Unicast
    Relay - Receivers:
      Unicasts,
      Subnet-specific broadcast, or
      Legacy IP mulitcast
    Drawbacks
      Management overhead (at Relays)
      Static topology between source and Relays
        Cannot reflect group-membership dynamics

## Slide 23: Application Level Multicast

## Slide 24: IP Addressing
  Class A (1/2): 0.0.0.0 - 127.255.255.255
  Class B (1/4): 128.0.0.0 - 191.255.255.255
  Class C (1/8): 192.0.0.0 - 223.255.255.255
  Class D (1/16): 224.0.0.0 - 239.255.255.255

## Slide 25: Unicast
Class A, B and C
  Today, all IP-based applications based on Unicast
Network Masking
  Network Number + Host Portion
  (11 --------11) (00 -------00)
  An Example
    168.188.12.34: Class B
    255.255.0.0/16: Network Mask
    In Case of Class A: 255.0.0.0/8
    In Case of Class C: 255.255.255/24

## Slide 26: Subnet Masking
Typical Subnet masking
  In Case of Class B: 168.188.0.0/16
    168.188.1.0/24, .., 168.188.254.0/24
VLSM (Variable Length Subnet Masking)
  22 bits of the Host Portion: Class A
  14 bits of the Host Portion: Class B
  6 bits of the Host Portion: Class C
Advantages
  Hierarchical Address Allocation within a domain
  Aggregation of Routing Information by Prefix
  RIPv2 & OSPF: classless intra-domain routing
  CIDR (Classless Inter-Domain Routing): From BGP4+
    VLSM applied to Inter-domain routing

## Slide 27: Broadcast
MAC Layer Broadcast
Subnet Broadcast
  Limited Broadcast
  All Subnets Broadcast
  Subnet-Specific Broadcast
Multicast IP over IEEE LANs
  Class D Multicast Address
  MAC Layer Multicast Address
  Mapping “Class D” to MAC Layer Multicast Address

## Slide 28: MAC Layer Broadcast
MAC layer broadcast
  Send a packet to all hosts on Subnet at once
  See Figure 2-6 in Textbook
  Broadcast Address
    0xFF-FF-FF-FF-FF-FF (48 bits)
    IEEE 802 LAN such as Ethernet and FDDI
Examples
  IP-based protocols on MAC-layer broadcast
    Routing Protocols & IGMP
  ARP (Address Resolution Protocol)
    MAC layer broadcast (IP header is not used)

## Slide 29: IP Subnet Broadcast (1)
Limited Broadcast (within a subnet)
  255.255.255.255
  Not forwarded off the subnet (within a subnet)
Subnet

## Slide 30: IP Subnet Broadcast (2)
All-Subnets Broadcast (within a domain)
  Network ID + all 1’s
    (Example) Class B: 190.45.255.255
  Broadcast Storm: Not recommended
Subnet
Subnet
Subnet
Domain

## Slide 31: IP Subnet Broadcast (3)
Subnet-Specific Broadcast
  Subnet ID + Host Portion (all 1’s)
    Example) Subnet: 190.45.104.0/22
      3rd octet: 011001xx
    Subnet-specific broadcast:190.45.107.255
      3rd octet: 011001 + 11 (104 + 3) = 107
    From an external host to another subnet
Subnet
Domain
Host
Subnet

## Slide 32: IP Multicast Address (1)
Class D Address
  224.0.0.0 - 239.255.255.255
Reserved Addresses
  IANA: RFC1700
  224.0.0.x/24 (See Textbook)
    For use of routing protocols, other lower-level topology discovery or maintenance
      224.0.0.1: All Systems on this Subnet
      224.0.0.2: All Routers on this Subnet, etc
  224.0.1.x/24 (See Textbook)
    Well-known addresses for certain applications
      224.0.1.1: NTP (Network Time Protocol), etc

## Slide 33: IP Multicast Address (2)
Other Reserved Addresses
  239/8: RFC 2365 (1998)
    “Administratively Scoped IP Multicasting”
    Within private networks such as enterprise networks or “Intranets”
  233/8: RFC 2770 (Feb., 2000)
    GLOP (Static Assignment) addressing
      (Confer) Dynamic Address Allocation
  232/8: SSM WG
    For Source Specific Multicast (SSM) Routing

## Slide 34: TTL Scoped IP Multicasting
Using TTL-Threshold
  Restrict the lifetime of Multicast Packets
  Complex to implement (TTL-Threshold measure)
    Unreliable: Routing Change
    DVMRP: undesirable pruning of tree

## Slide 35: Administratively Scoped Multicasting
Based on address (Regardless of TTL)
  Administratively Scoped IP Multicasting
    239/8 (239.0.0.0 - 239.255.255.255)
      Site-Local Scope: 239.253.0.0/16
      Organization-Local Scope: 239.192.0.0/14
  Globally scoped Addresses
    224.0.1.0 - 238.255.255.255

## Slide 36: GLOP (Static) Addressing
Static Allocation and Assignment
  IETF MboneD WG
    RFC 2770 (Feb., 2000)
    GLOP uses Autonomous System (AS) numbers
      2 Octets (Second and Third bytes)
      (e.g) AS 5662: 233.22.30/24
    Experiments will be reviewed in May 2000
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 233 | 16 bits AS | local bits |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 37: Multicast IP over LANs (1)
IEEE 802 MAC Address Format: 48 bits
  M: Unicast(0)/Multicast(1)
    MAC Broadcast address: 0xFF-FF-FF-FF-FF-FF
  L: Universal(0)/Local(1)
  OUI: Organizationally-Unique Identifier
    with L=0 and M=0
    IEEE sells “blocks” of MAC addresses
  Manufacturer: Uniquely assigned by Manufacturer
8
L
M
OUI (22)
Manufacturer (24)
24
48

## Slide 38: Multicast IP over LANs (2)
How to forward IP (unicast) Packet over a LAN
  - Masking (Network or Extended Network Prefix)
  1. Apply the Mask to the Destination Address
  2. Masked Destination Address of a Packet =
  Your Subnet’s Prefix ?
  - YES: Check the local ARP cache (go to 3)
  - NO : Forward the packet to the default Router
  (Based on the Configuration or Routing Table)
  3. If the destination address is not the ARP cache,
  Broadcast an “ARP Request” to ask its MAC address
  (The end host replies with “ARP Reply”)
  4. Send the Ethernet Frame to the end host
  by encapsulating the IP packet

## Slide 39: Multicast IP over LANs (3)
Forwarding of an IP Packet over LAN
  “Mask and Match” Procedure
R
Subnet
IP Packet
Prefix: 168.188.12/24
Destination Address: 168.188.12.23
Default Router
YES
NO
ARP Request & Reply

## Slide 40: Multicast IP over LANs (4)
Multicast Packet Forwarding over LAN
IGMP(Internet Group Management protocol)
  Router realizes who is a member in the Subnet
  Via IGMP Query & Report (with Class D address)

## Slide 41: Multicast IP over LANs (5)
Multicast MAC Address
  IETF’s OUI: 0x00-00-5E
  M bit = 1: thus, 0x01-00-5E (The first 24 bits)
  The next bit is reserved (always ‘0’)
    23 bits available for the multicast address
Mapping of Class D to Multicast MAC address
  Class D: the first bits are fixed to be ‘1110’
    28 bits : Group Unique Identifier
  Take the lowest 23 bits as MAC multicast address
24
48
0
01-00-5E
Lowest 23 bits of Class D

## Slide 42: Multicast IP over LANs (6)
An Example
  Class D address: 239.147.6.99
  Hex: EF-93-06-63
  Binary: 1110-1111, 1001-0011,0000-0110, 0110-0011
  Hex in MAC: 01-00-5E-13-06-63
Broadcast & Multicast
  In Broadcast, LAN NIC must receiver broadcasts
  But, Selectively receive the multicast packets
    If 23 bits are matched to the Class D address
    The NIC filters those matched multicast frames, which is passed up to the high layer software
      Note) Address Collision Possible !
    Undesired address (collision) will be ignored