## Slide 1
MBONE
기술과 응용
신명기
(mkshin@pec.etri.re.kr)
2000. 10.10

## Slide 2: Talk Outline
MBONE ?
Basic Concepts
  IP multicast, Tunnel, threshold, TTL ...
Applications
Guideline for MBONE Connection
MBONE-KR Status
Conclusions

## Slide 3: What’s in a Name ?
Multicast backBONE
Virtual Network on the Internet
  routers and hosts that support IP Muticasting
World Wide Experimental Network
  Protocols : IP Multicast, RTP, SDP & SAP/SIP
  Applications : Real-Time Interactive Multimedia Service
Tomorrow’s Multicast Internet

## Slide 4: History of the MBONE
IP Multicast
  developed by Steve Deering(CISCO) in 1988.
Audiocast from IETF in March 1992
  30 people participated from Australia, Sweden, the UK, US ...
IETF Boston meeting in July 1992
  the name “MBone” was coined during a dinner among Hans Eriksson, Steve Deering, and Steve Casner
  create the mbone mailing list
    mbone@isi.edu, rem-conf@es.net

## Slide 5: MBONE, Today
Reason MBONE Became Possible
  installation of high bandwidth Internet backbone connection
  widespread avalibility of powerful workstation
  developed protocols and applications supported IP multicast
Evolution and Development
  connects over 1700+ subnets in over 25+ countries
  multicast over 300+ international conference and event
  Evolution : IP Multicast Initiative(IPMI)
  Protocol : IETF WGs
  Application Developments: Various Vendors

## Slide 6: World Wide Topology

## Slide 7: Basic Concepts
IP Multicast
Mrouter and Tunneling
metric, threshold, and TTL
Bandwidth
Routing Protocols
Protocol Architecture

## Slide 8: IP Multicast
IP Multicast Addressing
  Ability to deliver an IP packet to group member
  Group idenfitied by Class D IP address
IGMP
  mrouter periodically sends “Host MemberShip Query”
  host replys for mrouter “Host MemberShip Report”
1110
host group
(224.0.0.0 ~ 239.255.255.255)
mrouter
g
g
g
Host MemberShip Query
Host MemberShip
  Report
subnet

## Slide 9: Tunneling & Mrouter
터널
인터넷연결
멀티캐스트 라우터
네트워크

## Slide 10: How Do Tunnel Work ?
IP Multicast Packets
  encapsulated for transmission through tunnel
  look like normal unicast datagram
H
m
Tunnel
Source
Tunnel
Dest.
Original
Source
Multicast
Dest.
IP Encapsulation
Normal Multicast Packet
Tunnel
Internet
Internet
H
m
Router
mrouter
host
data

## Slide 11: Tunnel Configuration
/etc/mrouted.conf
  tunnel <local_ip> <remote_ip> [metric] [threshold]
  examples
    tunnel 129.254.201.13 143.248.172.41 metric 1 threshold 32
멀티캐스트 라우터
네트워크
129.254.201.x
143.10.20.x
metric 1 threshold 32

## Slide 12: Configuration Option
metric
  represents the “cost” or “length” of the tunnel
  default = 1
  using multicast routing algorithms compute delivery paths with minimum sum-of-metrics
    31 <= metric summation of path no forwarding
threshold
  the minimum TTL(Time-To-Live) needed for a packet to be forwarded
  used to enforce resoure boundaries
    packet’s TTL value < tunnel’s threshold no forwarding

## Slide 13: TTL Limitation
TTL(Time-To-Live)
  each multicast packet carries, decremented by one at each multicast router
멀티캐스트 라우터
129.254.201.x
143.10.20.x
threshold 16
143.10.21.x
threshold 32
네트워크
(1)Sender’s Packet TTL=32
(2) Sender’s Packet TTL=31

## Slide 14: Multicast Routing
DVMRP
  Distance-Vector Multicast Routing Protocol
  Current routing protocol of the MBone(mrouted applied)
  Scaling Problem
MOSPF
  Multicast Extension to OSPF, No tunnuling
  Proteon, Inc., 3Com Corporation, “Sparce” group Problem
PIM
  Protocol Independent Protocol, dense mode / sparce mode
  Bay Networks, Inc.
CBT
  Core-Based Trees, Bay Networks, Inc.
  uses single spaning-tree for reduced control traffic for “sparce” group

## Slide 15: Bandwidth Constraint
Broadcast Quality
  14.4kbps : AM Radio, 1~3 frame/s
  28.8kbps : FM mono, AM Radio with still image
  T1(1.555Mbps) : CD quality audio, MPEG video
  ATM(155Mbps~622Mbps) : MPEG2 or higher
Bandwidth
  Network saturation
  Current design bandwidth =~ 500kbps
Multicast packet distribution control
  TTL(Time-To-Live) Truncation : mrouted
  Prunning : commercial routers

## Slide 16: Research Activities
Multicast Traffic Distribution
  multicast service model / addressing
Internet Service Model
  non-best effort service / reservation / admission control
Transport Protocol
  real-time delivery / receiver adaptation / synchronization
Conference Control
  loosely-coupled session / tightly-coupled session
Conference Discovery
  session advertisement / invitation
Security

## Slide 17: MBONE Architecture
IP/IP Multicast
IGMP
TCP
UDP
HTTP
RTP/RTCP
RSVP
Audio
Video
HTML
SAP
SIP
Shared
HTML/
WB
SDP
VAT
VIC
WWW
SDR
IP: Internet Protocol
IGMP: Internet Group Management Protocol
UDP : User Datagram Protocol
TCP: Transmission Control Protocol
RSVP :ReSource reserVation Protocol
RTP :Real Time Transport Protocol
RTCP: RTP Control Protocol
SAP: Session Announcement Protocol
SIP:Session Invitation Protocol
SDP: Session Description Protocol
VAT: Visual Audio Teleconferencing
VIC : VIdeo Conference
SDR : Session DiRectory
WB : White Board
Integrated Services Forwarding
WB

## Slide 18: MBone Applications
Audio
  LBL’s vat, UMass’s nevot, UCL’ rat
Video
  Xerox’s nv, LBL’s vic
Shared WhiteBoard, Shared Editor
  LBL’ wb, UCL’ nt
Session Management
  LBL’s sd, UCL’s sdr, USC-ISI’s mmcc
Shared HTML
  EIT’s shared Mosaic, ENST’s mMosaic, CDT’ mWeb, INRIA’s WebCanal
On-Demand
  MBONE VCR, IMJ, mMOD

## Slide 19: vat
visual audio teleconferencing tool from LBL
  ftp://ftp.mbone.or.kr/mbone/applications/vat/*
Feature
  based on the Real-time Transport Protocol (RTP)
  for Sun, SGI, HP, Linux ... and Windows 95
vat 224.2.0.1 / 3456

## Slide 20: vic
video conference tool from LBL
  ftp:// ftp.mbone.or.kr/
  mbone/applications/vic/*
Feature
  based on the Real-time Transport Protocol (RTP)
  for Sun, SGI, HP, Linux ... and Windows 95
vic 224.9.1.1 / 5554

## Slide 21: wb
Shared white board from LBL
  ftp:// ftp.mbone.or.kr/
  mbone/applications/wb/*
Feature
  import postcsript, text
  for Sun, SGI, HP, Linux
wb 224.2.1.5 / 5555

## Slide 22: sdr
session directory from UCL
  ftp:// ftp.mbone.or.kr/
  mbone/applications/sdr/*
Feature
  allow the advertise and joining of multicast conferences on the MBone
  implements SDP, SIP, SAP protocol
  Unix(HPUX, IRIX, SUNOS4.1.x, Solaris2.x) and Windows 95
sdr

## Slide 23: Conference Control
Loosely-coupled Session
  used on MBone
  no session membership, session control
  RTP/RTCP over UDP, IP multicast
  only user-id(eg, mkshin@pec.etri.re.kr) using RTCP
Tightly-coupled Session
  ITU-T 124 GCC(Generic Conference Control)
  no Internet Standard
  session membership, session control

## Slide 24: Session Advertisement
v=0
o=mkshin 2890844521 2890842809 IN IP4 129.254.201.13
s=KRnet’97
i=A Tutorial Live on MBONE
u=http://pec.etri.re.kr/KRnet97/index.html
e=mkshin@pec.etri.re.kr (Myung-Ki Shin)
c=IN IP4 224.4.12.12/15
t=3034423619 30424624219
m=audio 2222 VAT PCM
m=video 3333 RTP H261
m=whiteborad 4444 UDP WB
a=orient:landscape
sender
receiver
SDP
SAP
SAP
멀티캐스트 라우터
네트워크
네트워크
receiver
멀티캐스트 라우터

## Slide 25: New Multimedia Service
Internet Broadcasting Service
  Audio-video service on Computer as same as Home TV
    IP/TV, Vosaic, etc.
Multicast WWW
  New Cache Model
  Remote Presentation
    Shared Mosaic, Webcast, mMosaic, mWeb, WebCanal ...
Integrated Multimedia Services
  Audio+Video+WWW+E-mail ....

## Slide 26: Internet TV
Precept’s IP/TV
  used to send or receive video broadcasts on the Internet
  http://www.precept.com
  IP/TV Server
  IP/TV Viewer
  Program Guide
    allows easy scheduling of session

## Slide 27: IP/TV
IP/TV Viewer
Program Guide
http://www.precept.com/cgi-bin/
iptv/iptvmain.pl

## Slide 28: MBONE Connection
System Requirements
  Requirements of Hardware platform
  UNIX, PC, Macintosh, etc.
  Multimedia peripherals : audio, video (optional)
Connection to MBONE
  Connection to Internet
  IP Multicast kernel patch
  Installation of “mrouted”
  Tunneling request
  Tunnel configuration & Tunneling

## Slide 29: System Requirements
UNIX
  SunOS, Solaris, IRIX, HP-UX, OSF/1, AIX, etc.
  OS version에 따라 일부 kernel patch 필요
  download patch programs
    ftp://ftp.mbone.or.kr/mbone/applications/ipmulticast/*
PC, Macintosh
  IP Multicasting 지원
  Dose NOT support multicast packet routing
    cannot be a mrouter ( = cannot have a tunnel)
  windows98/windowsNT, Mac OS

## Slide 30: System Requirements
Multimedia Peripherals
- Audio
  Choose the proper Audio card for your hardware platform
  Receiver side : speaker
  Sender side : speaker + microphone
- Video
  Choose the proper Video grabber card for your hardware platform
  Sender side : camera

## Slide 31: System Requirements
UNIX Platform
  patch programs
  ftp://ftp.mbone.or.kr/mbone/applications/ipmulticast/*
Machines
Operating Systems
Sun SPARC
DEC Station
Hewlett Pckard
Sillicon Graphics
RS/6000
SunOS 4.1.x
Solaris 2.x
(커널수정)
OSF/1 1.3
OSF/1 2.x, 3.0
(커널수정)
HP-UX 9.0.x
AIX 3.2.5
All multicast support

## Slide 32: Connection to Internet
MBONE is not a physical network !!
  Don’t need additional connection for MBONE
  Don’t need extra fee for MBONE feeding
MBONE is a logical network on the Internet
  Current your ISP can provide MBONE feeding
First, connect to the Internet !!

## Slide 33: Installation of “mrouted”
mrouted
  is implemented by DVMRP
  supports Multicast packet routing through Tunnel
  current mrouted version 3.8 (96.10.31 MBONE 권고사항)
    draft-ietf-mboned-pruning-01.txt “Multicast prunig a necessity”
program
  ftp://ftp.mbone.or.kr/mbone/applications/mrouted/*
must be “root”
  % /etc/init.d/mrouted start
  % /usr/multicast/mrouted -d 9
  % kill `cat /etc/mrouted.pid`

## Slide 34: Tunneling Request
Tunnel
  Virtual point-to-point link for Multicasting
  mrouted tunnel : DVMRP tunnel
  router-based tunnel : PIM tunnel, GRE tunnel (Cisco)
Tunneling request (Domestic)
  mbone@mbone.or.kr

## Slide 35: Tunneling Request
Example : tunnel 신청 메일
  mail to : mbone@mbone.or.kr
  Subject : Mbone 터널링 요구
    사용기관 : KORNET
    mrouter IP : 147.6.9.91
      (터널링 하고자하는 자신의 host IP address)
    version : mrouted 3.8
    소속기관 : 한국전자통신연구원
    담당자 : 신명기(mkshin@pec.etri.re.kr)
    기타 …

## Slide 36: Tunnel Configuration
Tunnel types
  mrouted tunnel
    file : /etc/mrouted.conf (plain text file)
  router-based tunnel
    PIM tunnel (Cisco router configuration)
Configuration parameters
  tunnel의 source, destination 설정
    metric, threshold, rate_limit
  tunnel의 attribute parameter 설정 (optional)
    phyint, cache-lifetime, pruning

## Slide 37: Tunnel Configuration
Example : mrouted tunnel
  /etc/mrouted.conf
phyint <local-addr> [disable] [metric <m>]
tunnel <local-addr> <remote-addr> [metric <m>]
[threshold <t>] [rate-limit <b>]
cache-lifetime <ct>
pruning <off / on>
  Example : h2o.kotel.co.kr
tunnel 147.6.1.77 203.234.255.134 metric 1 threshold 32

## Slide 38: Tunneling
must be ROOT
  % /etc/mrouted start
  % /usr/multicast/mrouted -d 9
  % kill `cat /etc/mrouted.pid`
Tunnel monitoring utilities
  mrinfo : target mrouter의 터널정보 및 버젼 표시
  % /usr/multicast/mrinfo mrouter-ip-address
  mtrace : target mrouter까지의 경로 및 트래픽 정보수집
    % /usr/multicast/mtrace mrouter-ip-address

## Slide 39: Tunneling
Example : mrinfo (localhost)
  %/usr/multicast/mrinfo
    127.0.0.1 (localhost) [version 3.8,prune,genid,mtrace]:
    147.6.1.77 -> 0.0.0.0 (local) [1/1/querier/leaf]
    147.6.1.77 -> 203.234.254.1 (streamwk.kix.net) [1/16/tunnel]
    147.6.1.77 -> 143.248.185.2 (maple.kaist.ac.kr) [1/32/tunnel]
    147.6.1.77 -> 147.47.1.8 (nms.kren.nm.kr) [1/32/tunnel]
    147.6.1.77 -> 147.6.9.91 (disney.kotel.co.kr) [1/16/tunnel/down/leaf]
    147.6.1.77 -> 147.6.9.123 (mong.kotel.co.kr) [1/16/tunnel]
    147.6.1.77 -> 147.6.14.172 (luna.kotel.co.kr) [1/16/tunnel/down/leaf]
    147.6.1.77 -> 147.6.22.91 (longdari.kotel.co.kr) [1/16/tunnel/down/leaf]

## Slide 40: MBONE-KR (I)
’92. 최초 MBOBNE Audiocast 시 Korea 지역망
획득 (25th IETF 참여)
  mbone-korea@cosmos.kaist.ac.kr
  해외터널 구성 (cosmos.kaist.ac.kr, 56Kbps)
’93. 해외 MBONE 터널 변경
  h2o.kotel.co.kr, 256KBps, Threshold 128
’94. 국내 최초 MBONE 화상회의 시연
  KAIST - ETRI - SERI - NCA

## Slide 41: MBONE-KR (II)
’95. 7. KRNET95 전시회 MBONE 시연
  MBONE BOF 미팅 (MBONE 사용자 그룹 결성)
  국내 MBONE Web Server 구축 (www.mbone.or.kr)
’96. 3. 국내 최초 MBONE 행사 중계
  제3회 WWW-KR 워크샵 (부산대)
’96. 5. Internet-KIG MBONE WG 발족
  OSIA 산하 Internet Working Group

## Slide 42: MBONE-KR (III)
’96. 7. I*EXPO 해외 MBONE 터널 구성
  eix-mbone1.kix.net, 45MBps, Threshold 64
  최초 해외 MBONE 행사 중계 (KRNET96 워크샵)
’96. 12. 제1회 MBONE-KR 총회 개최
  한국인터넷협회(KRIA) 산하 Technical Working Group 등록
’97. 3. 제1회 인터넷 운영 워크샵 참가
  MBONE-KR BOF, MBONE-WG 회의개최

## Slide 43: MBONE-KR (IV)
’97. 3. MBONE 사용자 설명서 발간
  “차세대 멀티미디어 인터넷 : MBONE 해부”
’96. 6. MBONE-KR 조직 구성
  mbone.or.kr domain 등록
  mbone@mbone.or.kr
’97. 7. KRNET97 워크샵 해외 중계
참고 : htp://www.mbone.or.kr/history/

## Slide 44: MBONE-KR Status
MBONE-KR 조직구성
  망관리분과 : 국내 MBONE 망 구축 및 관리
  기술분과 : multicasting 관련 기술연구 (MBONE-WG)
  중계분과 : MBONE 중계지원 및 관련기술 확보
가입기관
  40여개 기관 (T1급)
  120여개 mrouter 운영중
MBONE-KR 메일링리스트 가입
  약 300명 (mbone@mbone.or.kr)

## Slide 45: MBONE-KR Topology
eix-mbone1.kix.net
h2o.kotel.co.kr (KTRL)
KIX/KT
maple.kaist.ac.kr (KAIST)
Shinbiro
www.kreonet.re.kr
nms.kren.nm.kr
kIX/CS
1997.5.26 mbone-sec@knc.or.kr
64
tomcat.nca.or.kr
32
32
32
streamwk.kix.net
16
snow.postech.ac,kr(POSTECH)
paro.etri.re.kr(ETRI)
athena.kwangwoon.ac.kr(Kwangwoon Univ.)
kwanak.nowcom.co.kr
32
16
doit.ajou.ac.kr
(Ajou Univ.)
203.247.198.101(동명정보대)
16
32
oslab.snu.ac.kr
(SNU)
mmlab.snu.ac.kr
(SNU)
proxy.kangwon.ac.kr
(Kangwon Univ.)
ced.kyungsung.ac.kr
(Kyungsung Univ.)
hawk.uriel.net
snow-man.inet.co.kr
203.241.151.12(SDS)
KORNET
International
Mbone
gsl-stock-ns.gsl.net
mong.kotel.co.kr
hilib.kotel.co.kr
hist.kotel.co.kr
cscw.kwangwoon.ac.kr
zoot.hanyang.ac.kr (Hanyang Univ.)
203.251.135.22 (KBS)
suny.yonsei.ac.kr (Yonsei Univ.)
nod.korea.ac.kr (Korea Univ.)
IVYNET
NOWNURI
NURINET
NEXTEL
gentle.kyungsung..ac.kr
16
cimerr.postech.ac.kr
amazon.postech.ac.kr
logos.hanyang.ac.kr (Hanyang Univ.)
www.nada.co.kr(나다기연)
tenet3.kyungpook.ac.kr
(Kyungpook Univ.)
134.75.207.102
coven.dongseo.ac.kr
(Dongseo Univ.)
cadiones.kaist.ac.kr
pegasus.dongseo.ac.kr
comin.dongseo.ac.kr
dalab.dongseo.ac.kr
core.chungnam.ac.kr
(Chungnam Univ.)
203.252.134.46
32
210.124.156.66
210.120.37.18
BORANET
white.dacom.co.kr
8
KREN
KREONET
matrix.shinbiro.com
202.30.199.5
saxophone.shinbiro.com
32
32
anova.inha.ac.kr
(Inha Univ.)
balad.lge.co.kr
(LG Electronics)
h2o.hansol.co.kr
wonhyo.dongguk.ac.kr
(Dongguk Univ.)
rabbit.sookmyung.ac.kr
(Sookmyung Univ.)
cssun10.cs.hangkong.ac.kr
(Hangkong Univ.)
ElimNet
32
dino.elim.net
movie.internex.co.kr

## Slide 46: Domestic Threshold Guideline
Purpose
  광대역 데이타 (화상/음성 등)로 인한 네트웍 낭비의 최소화
  국내 Unicast routing 구조를 고려한 계층적 설정
Tunnel Threshold
국내 (KIX/KT) <---> 해외 (GSL)
KIX/KT <---> ISP MBONE node
ISP MBONE node <---> 개별기관
개별기관내
64
32 (48)
32
16

## Slide 47: Domestic TTL Guideline
Criterion
  자신의 외부 tunnel threshold와 비교, 원하는 전송범위 설정
  Session TTL < External Tunnel Threshold
Session TTL
해외 중계
국내 중계
개별기관내
구 분
TTL
example
  65 이상 (127)
  63 이하 (63)
15 이하 (15)
KRNET ‘97 Workshop
KBS 1 TV Live
Internet Team meeting

## Slide 48: Broadcast Guideline
500Kbps이상 (T1) 인터넷 접속 권고
  약 100 ~ 300 Kbps / session
Session announce
  중계기관은 프로그램 내용을 메일링리스트를 통해 사전 공고
  중계 안내 방법
    국내 중계 : mbone@mbone.or.kr
    해외 중계 : rem-conf@es.net
Technical support
  volunteer group (MBONE-KR)
  mbone@mbone.or.kr 메일링 리스트를 통해 도움 요청

## Slide 49: Mailing Lists
Worldwide
  mbone@isi.edu : MBONE User’s Group
  rem-conf@es.net : 기술문의, session announce
MBONE-KR
  mbone@mbone.or.kr : 국내 MBONE User’s Group
  mbone-wg@pec.etri.re.kr : Internet-KIG Multicast Group

## Slide 50: Resources
Book
  MBone : Interactive Multimedia on the Internet, New Riders, 1995
  MBone : Multicasting Tommorrow’s Internet, IDG, 1996,http://www.northcoast.com/savetz/mbone/toc.html
  차세대 멀티미디어 인터넷 : MBONE 해부 : MBONE-KR, http://lanman.tit.ac.kr/
Information Web
  http://www.mbone.com/
  http://www.mbone.or.kr/

## Slide 51: Conclusions
MBONE
  Virtual, Experimental IP multicast testbeds
  Tunnel, threshold(TTL), bandwidth, data compression, protocols ...
Feature
  Architecture composed of protocols & Service
  Application : vic, vat, wb, sdr ..... WWW Browser
  MBone has potential, because controlled by the people, not by companies
New Internet Services on MBone
  Web TV, Internet TV, Integrated Multimedia Services ....
MBone and Internet will be one entity