## Slide 1: IP Multicast Routing Overview
<Chapters 4 - 6 in Textbook>
Seok Joo Koh

## Slide 2: Table of Contents
Multicast Traffic Scoping
  TTL-based Scoping
  Administrative Scoping
Internet Group Management Protocol
  IGMPv1
  IGMPv2
  IGMPv3: overview
Multicasting Routing and Forwarding

## Slide 3: Multicast Traffic Scoping
Control the scope of multicast forwarding
  In terms of router hops
  How far the multicast transmission may propagate?
Two ways
  TTL based scoping: Being used in MBONE
  Administrative scoping
Implicit Scoping (?)
  Implicitly scoped address
    Generally reserved multicast address
    224.0.0.0/24 (within a subnet)
    “Link-Local” address
  Not forwarded, regardless of TTL

## Slide 4: Basics: Communications
Layering Concept
Higher Layer
IP
Data Link
Physical
Higher Layer
IP
Data Link
Physical
H
H
H
Payload
Encapsulation

## Slide 5: IP Packet Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
RFC 791: Internet Protocol

## Slide 6: TTL-based Scoping
TTL is decreased by 1
  Each time a router forwards a packet
TTL-Threshold
  A multicast router will only forward a multicast datagram across an interface, if the TTL field in the IP header is greater than the TTL threshold
Conventional TTL Scope Control Values
  TTL Scope Threshold
  0 Same Host
  1 Same Subnetwork
  15 Same Site
  63 Same Region
  127 Worldwide
  255 Unrestricted in Scope

## Slide 7: TTL Threshold
For each interface of a Router

## Slide 8: TTL Scoped IP Multicasting
Restriction to IP Multicast Packets
  TTL limits are related to Bandwidth limits
    Larger TTL: Lower bandwidth streams

## Slide 9: TTL-based Multicast Scoping: Limits
Depends Only on the TTL
  Not Per-Source, Per-Group
Requires Sender to know
  how far away authorized receivers are ?
  If a new subnet (receiver) is created ?
    that is one hop further away
TTL purposes (semantically overloaded):
  Limits the lifetime of a packet,
  Packet confinement due to bandwidth, and ..
Suitable choices of TTL is difficult
  At the Edge of the network or Internal
Intranet manager vs. Source Users
  Users may render the TTL-threshold ineffective

## Slide 10: Administrative Scoping
Overview
  Originally presented to IDMR WG session in 1994
  Scoping based on Multicast Address (not TTL)
  239/8: RFC 2365 (1998)
Features
  A mechanism for well-defined boundaries
  Privacy and Address Reuse by multiple domains
    Valid only with a Corporate network
    Not forwarded beyond the scoped boundary
Requirements
  Each router must block packets destined for 239/8 from leaving its site (from arriving at the site)

## Slide 11: Address for Administrative Scoping
  Administratively Scoped IP Multicasting
    239/8 (239.0.0.0 - 239.255.255.255)
    Recommendations in RFC 2365
      Admin. “Local” Scope: 239.255.0.0/16
      Site-Local Scope: 239.253.0.0/16
      Organization-Local Scope: 239.192.0.0/14
  Globally scoped Addresses
    224.0.1.0 - 238.255.255.255
  Benefits
    Does not depend on TTL
    Overlapping of admin. Scoped domains:
      Figure 4-4 in text
  Usage Guidelines for Admin. Boundary: Figure 4-5

## Slide 12: Internet Group Management Protocol
Overview
  Between a router and hosts within Subnet
  Only interested hosts receive the IP multicast traffic for any given group
  IGMP is the signaling protocol
    that end hosts use to signal their group membership interests
    Members must tell the routers what groups interest them
  IGMP is an integral part of IP
    Essential to IP multicasting
  IGMP version 1: RFC 1112 (1988)
  IGMP version 2 : RFC 2236 (1997)
  IGMP version 3: Internet Draft (IDMR WG)

## Slide 13: IGMPv1
Protocol Overview
  A router periodically transmits <Host Membership Query> messages to the hosts in its subnet
    over 224.0.0.1, IP TTL = 1
  When a host receives IGMP Query, it responds with a <Host Membership Report> for each group (G) it belongs
    over the class D address G, not 224.0.0.2
  Why send Report(G) over G, not 224.0.0.2 ?
    Multicast Router can promiscuously receive all multicast IP traffic
    Make Router’s job easy
    Report Suppression (described later)

## Slide 14: IGMPv1 Operations
Query & Report(G)

## Slide 15: IP Header + IGMPv1 Header
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| Type | Unused | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 16: IGMPv1 Messages
IGMPv1 Query
  IP packet source = Router IP address
  IP packet destination = All hosts (224.0.0.1)
  IP Protocol = 2 (IGMP)
  IGMPv1 Version = 1 (0001)
  IGMPv1 Type = 1 (0001)
  IGMPv1 Group address = G (class D)
IGMPv1 Report
  IP packet source = Host IP address
  IP packet destination = G (class D)
  IP Protocol = 2 (IGMP)
  IGMPv1 Version = 1 (0001)
  IGMPv1 Type = 2 (0010)
  IGMPv1 Group address = G (class D)

## Slide 17: IGMP Report Suppression
Each host responds with Report to Query
  If there exist so many hosts for the group,
    then Report Explosion !
Random-timer based Report Suppression
  Each host starts a random <Report delay> timer
    Before it sends an IGMP Report
  If the timer expires, then it sends the Report
  If any other host sent the Report for the same G
    then it resets its timer to a new random value
    The random time is ranged by
      [0, Maximum Response Time]
      Usually, in units of 1/10 seconds

## Slide 18: NOTE
A multicast router is not required to maintain
  a detailed list of which hosts belong to the G
  how many members are there
A multicast router only needs to know
  whether at least one group member is present on a given interface
A multicast router periodically transmits IGMP Query messages to refresh its group information
  If no report(G) from any host for a time,
    the router assumes no membership in the subnet
When a host first joins a group,
  it does not wait for a Router’ Query
  it immediately transmits a Report(G)
  to minimize the Join Latency

## Slide 19: IGMPv2
IGMPv2 along with DVMRP
  “mrouted” (version 3.3) source code for MBONE
  Initially, only the source code
  RFC 2236 (1997)
  All modern IP multicast implementation: IGMPv2
Features
  Lowering the Leave Latency
  Two New messages are defined
    IGMPv2 Leave Group
    IGMPv2 Group-Specific Query
  In response to Leave Group
    Router sends Group-Specific Query

## Slide 20: Packet Format: IGMPv1 & IGMPv2
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Max Resp Time | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| Type | Unused | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
IGMPv1
IGMPv2

## Slide 21: IGMPv2 Packet Types

## Slide 22: Leave Latency
Leave Latency is measured between two times
  LAN’s last group member sends its last Report
  Router stops forwarding traffic for that group
In IGMPv1
  How could Router know if there is a member in the subnet ?
  Only way is to wait several Query interval to pass without hearing a Report from any group member
    Minimum of three Query intervals
IGMPv2 reduces the Leave Latency
  Leave Group (G) by Host
  Group-Specific Query (G) by Router
  Report by any other group member

## Slide 23: IGMPv3
IDMR WG <draft-ietf-idmr-igmp-v3-04.txt>
IGMPv2(G) => IGMPv3(S,G)
Support Group-Source Report message
  End host can elect to receive traffic only from specific sources sending to a multicast group
  Source Filtering
    Inclusion Group-Source Report (G, S*)
    Exclusion Group-Source Report (G, S*)
Benefits
  Unauthorized sources
  Unnecessary multicast traffic (save bandwidth)
Relationship with SSM
  Source Specific Multicast

## Slide 24: Implication of IGMP
IGMP
  Interaction between Router and Hosts
  Within a Subnet
  Group Membership Information for Router
In Multicast Routing Protocols,
  We do not need to consider Individual Hosts
  Routers keep Group-Membership in the subnet
  We have only to concern the interactions between Routers, to build a multicast tree

## Slide 25: Multicast Routing & Forwarding
Multicast Routing Protocols (MRP)
  used by multicast routers to discover delivery paths(trees) for forwarding of multicast datagram
Multicast Forwarding
  done based on information derived from MRP
    From an Input interface
    To one or more Output interfaces
Terminology
  Distribution (Delivery) Tree
  Upstream : toward Source
  Downstream : From Source

## Slide 26: Multicast Routing Protocols
DVMRP: RFC 1075 (1988)
  Distance Vector Multicast Routing Protocol
MOSPF: RFC 1585 (1994), RFC 2178 (1997)
  Multicast Extensions to OSPF
PIM-DM: Internet Draft
  Protocol Independent Multicast - Dense Mode
CBT:RFC 2201 (1997), RFC 2189 (1997)
  Core Based Tree
PIM-SM: RFC 2117 (1997), RFC 2362 (1998)
  Protocol Independent Multicast - Sparse Mode
New: Simple Multicast, SSM
Others (for Inter-Domain)
  H-DVMRP, H-PIM, O-CBT, BGMP/MASC, MSDP/M-BGP, ..

## Slide 27: Classification of MRP
Broadcast & Prune (Data-Driven)
Tree Types
  Shared Tree
  Source-Specific Tree
Join Types
  Implicit Join (Data-Driven)
    Assume) A router joined all Groups by default
  Explicit Join
    Explicit Join Message and Mechanism
Dense Mode vs. Sparse Mode
Intra-Domain vs. Inter-Domain

## Slide 28: Broadcast and Prune (1)
Used by DVMRP
Data-Driven (Implicit Join)
Broadcast (Reverse Path Broadcast)
Prune (if a subnet has no group member)
RPB(Reverse Path Broadcasting)
  Flooding + Reverse Path
TRPB(Truncated RPB)
  RPB + Truncate (based on IGMP)
RPM (Reverse Path Multicasting)
  TRPB + Prune + Grafting

## Slide 29: Broadcast and Prune (2)
First Broadcast, Then Prune !
S
Prune Message
R
R
Parent Link
Child Link
Prune Message

## Slide 30: Two Tree Types
Source Based Tree
  Shortest-path tree from Sender to Receivers
  data-driven: After the data arrived at the router
  DVMRP, PIM-DM, MOSPF
Center Based Tree (Shared Tree)
  Center (node or router)
    Core (CBT), Rendezvous Point (PIM-SM)
  One Center per One Multicast Group
  All Router (Source & Receivers) join the Core !
  Explicit Join
    From Receiver Router to Core Router

## Slide 31: Source Based Tree
Shortest Path Tree from Source to Receivers
Source
R
R
R

## Slide 32: Shared Tree
Shortest Path Tree from Core to Sender and Receivers
Source
R
R
R
Core
R

## Slide 33: Two Join Types
Implicit Join (or Data Driven)
  Assume that Routers are member for all Group
  Hosts <=> Router (Subnetwork)
  Tree Configuration after Data arrived at the Router
  DVMRP, PIM-DM
Explicit Join
  Explicit Join message from Router to Core
  Hosts <=> Router (Subnetwork)
  Router <=> Core (Network)
  Tree Configuration from Router to Core
  CBT, PIM-SM
NOTE) MOSPF = Source Based Tree + non-implicit Join
NOTE) SSM = Source Based Tree + Explicit Join

## Slide 34: Implicit Join
Data Driven
Subnet
R
R
Router
Source
Multicast Data

## Slide 35: Explicit Join
Host <=> Router <=> Core Router
Router
Center
Multicast Data
Router
S
R
Join 메시지
IGMP
IGMP

## Slide 36: Multicast Routing Protocols