## Slide 1: Multicast Routing Protocols in Sparse Mode
Seok Joo Koh

## Slide 2: Table of Contents
Review
Core Based Tree (CBT)
Protocol Independent Multicast - Sparse Mode
Simple Multicast (SM)
Source-Specific Multicast (SSM)
QoS-based Multicast Tree

## Slide 3: IGMP
IGMPv1: Query & Report(G)
IGMPv2: Lower Leave Latency
  Leave Group(G) & Group-Specific Query(G)
IGMPv3 (S,G): Source Filtering

## Slide 4: Multicast Routing Protocols

## Slide 5: MBONE-KR
eix-mbone1.kix.net
h2o.kotel.co.kr (KTRL)
KIX/KT
maple.kaist.ac.kr (KAIST)
Shinbiro
www.kreonet.re.kr
nms.kren.nm.kr
kIX/CS
1997.5.26 mbone-sec@knc.or.kr
64
tomcat.nca.or.kr
32
32
32
streamwk.kix.net
16
snow.postech.ac,kr(POSTECH)
paro.etri.re.kr(ETRI)
athena.kwangwoon.ac.kr(Kwangwoon Univ.)
kwanak.nowcom.co.kr
32
16
doit.ajou.ac.kr
(Ajou Univ.)
203.247.198.101(동명정보대)
16
32
oslab.snu.ac.kr
(SNU)
mmlab.snu.ac.kr
(SNU)
proxy.kangwon.ac.kr
(Kangwon Univ.)
ced.kyungsung.ac.kr
(Kyungsung Univ.)
hawk.uriel.net
snow-man.inet.co.kr
203.241.151.12(SDS)
KORNET
International
Mbone
gsl-stock-ns.gsl.net
mong.kotel.co.kr
hilib.kotel.co.kr
hist.kotel.co.kr
cscw.kwangwoon.ac.kr
zoot.hanyang.ac.kr (Hanyang Univ.)
203.251.135.22 (KBS)
suny.yonsei.ac.kr (Yonsei Univ.)
nod.korea.ac.kr (Korea Univ.)
IVYNET
NOWNURI
NURINET
NEXTEL
gentle.kyungsung..ac.kr
16
cimerr.postech.ac.kr
amazon.postech.ac.kr
logos.hanyang.ac.kr (Hanyang Univ.)
www.nada.co.kr(나다기연
tenet3.kyungpook.ac.kr
(Kyungpook Univ.)
134.75.207.102
coven.dongseo.ac.kr
cadiones.kaist.ac.kr
core.chungnam.ac.kr
(Chungnam Univ.)
203.252.134.46
32
210.124.156.66
210.120.37.18
BORANET
white.dacom.co.kr
8
KREN
KREONET
matrix.shinbiro.com
202.30.199.5
saxophone.shinbiro.com
32
32
anova.inha.ac.kr
(Inha Univ.)
balad.lge.co.kr
(LG Electronics)
h2o.hansol.co.kr
wonhyo.dongguk.ac.kr
(Dongguk Univ.)
rabbit.sookmyung.ac.kr
(Sookmyung Univ.)
cssun10.cs.hangkong.ac.kr
(Hangkong Univ.)
ElimNet
32
dino.elim.net
movie.internex.co.kr

## Slide 6: CBT & PIM-SM
CBT
  Bootstrap Mechanism
  Explicit Join from Router to Core Router
  Bi-directional Tree
PIM-SM
  Bootstrap Mechanism
  Explicit Join From Router to Redenzvous Point(RP)
  Uni-directional Tree
    Unicast (Tunneling) from Sender to RP
    (Uni-directional)Multicast from RP to Receivers
  SBT is allowed for high data rate (for a source)
    For low delay

## Slide 7: Bootstrap Mechanism
Discovery of Core (RP) for a Group
  In a Domain (Region)
  Mapping from Group to a Core or RP
    Group Address (Class D)
    IP address of a Core or RP
Assumptions
  One or more BSR (Bootstrap Router)
    Possibly dynamic election of BSR
  One or more Candidate Core(RP) Routers
  Both are configured by Network Manager

## Slide 8: Bootstrap Mechanism: Example
R
R
R
BSR
Bootstrap Message
(Active Core List)
Advertisement message
Core
Core

## Slide 9: Advertisement message by Core
Candidate Core(RP) Advertisement (C-RP-Adv)
  From Candidate Core to BSR
  Periodic Unicast
    Period Interval less than Hold-Time (below)
    The information may be updated
Information contained in C-RP-Adv message
  IP address of the Core (RP)
  Group Prefix (that the Core will cover)
    Group Address (G) & Mask Field (M)
  Hold-Time (valid duration), etc

## Slide 10: Bootstrap message by BSR
BSR creates the RP-Set
  Based on the C-RP-Adv messages
RP-Set contain the information for each C-RP
  IP address of the C-RP
  Group Prefixes (with Group Masks)
  Hold-Time, etc
BSR broadcasts Bootstrap message
  including the RP-Set

## Slide 11: Hash Function by Router
All (CBT & PIM) Routers
  Collect RP-Set information by Bootstrap messages
  Store and Updates them
When a Group(G) Join indicated by IGMP
  Run the Hash Function
    For the Cores with the same Group Prefix (G&M)
  Hash Function: Value = f(G, M, C(i))
    G = Requested Group Address
    M = Group Mask
    C(i) = IP address of Core
  For the Cores with Same group Prefix
    Select the highest Hash Value !

## Slide 12: Hash Function
Map a Group address to a unique Core(RP)
  Value = {1103515245 * ([1103515245 * (G&M) + 12345] XOR C(i)) + 12345 } mod 2^31
  For i = 1, 2, .. C
Based on only IP addresses (Core and Group)
  No Group membership Distribution Information
  High tree cost & Delay
Group Prefix of Candidate Cores must be set
  to cover all the group addresses

## Slide 13: CBT: Overview
A New Group by IGMP Report
  The Router detects a New Group by IGMP Report
Core Selection for the Group
  The Router runs the Hash Function
JOIN-REQUEST from Router to Core
  Router send JOIN-REQUEST message Toward Core
  Delivered by Unicast Routing Protocol
    Hop-by-Hop fashion
    Until active CBT branch is reached
  Forwarding Table: transient Join State
Join-ACK from a on-tree router to the Router
  Forwarding Table: Active State

## Slide 14: CBT: Join mechanism
Core
G
G
G
Join Request
Join ACK

## Slide 15: CBT: Forwarding Cache
Established by CBT Join-Request & Join-ACK
Forwarding Cache Form : (*, G)
  (Group, {outgoing interface list})
  Forward data (G) to all the interfaces
    except the incoming interface
Bi-directional Forwarding
  Simple (without Source field)
  No tunneling from sender to core
    cf. PIM-SM
    cf. Non-member Sending in CBT

## Slide 16: CBT: Maintenance
ECHO Protocol
  To maintain the tree
    ECHO-REQUEST: from child to parent router
    ECHO-REPLY: from parent to child router
When a upstream link or router fails
  FLUSH-TREE message on the downstream interfaces
  Reconstruction of tree by each router
    which has one or more attached members

## Slide 17: CBT: Echo Protocol
Core
G
G
G
Echo Request
Echo Reply

## Slide 18: CBT: Flush Tree
Core
G
G
G
Flush Tree
Join Request

## Slide 19: CBT: Non-member Sending
Sender-Only User
  IP-in-IP tunnel to Core from the router
Core
S
G
G
Unicast IP-in-IPTunnel
G

## Slide 20: PIM-SM: Overview
RP Selection by Hash Function
A New Group State by IGMP
RP-based Shared Tree (RP-Tree) Construction
  PIM Join from Router to RP
    Unidirectional RP-Tree
  PIM-Register message of Source (Tunneling)
    Encapsulation of Source Data to RP
  PIM-Register-Stop (native forwarding)
    SPT(Shortest Path Tree) from RP to Source(S)
Shortest Path Tree (SPT) Switching
  Switch from RP-Tree to SPT for S
    For high data-rate source (low delay)
  A Receiver’s Router initiates SPT construction

## Slide 21: PIM-SM: RPT (RP-Tree)
RP
S
G
G
PIM-Register
(Encapsulation)
PIM Join (*,G)

## Slide 22: PIM-SM: Forwarding on RPT
RP
S
G
G
PIM-Register
(Encapsulation)

## Slide 23: PIM-SM: PIM-Register-Stop (1)
RP
S
G
G
(S,G) Join

## Slide 24: PIM-SM: PIM-Register-Stop (2)
Encapsulation/De-capsulation Overhead at RP
  SPT from Source to RP (per source)
RP
S
G
G
Native Forwarding
on SPT
PIM-Register-Stop

## Slide 25: PIM-SM: SPT Construction
For Lower Delay: Optional (?)
  For high data rate (Data Rate Threshold)
RP
S
G
(S,G)
(S,G) Join

## Slide 26: PIM-SM: Forwarding on SPT
For Lower Delay: Optional (?)
  For high data rate (Data Rate Threshold)
  Initiated by the Receiver Router
RP
S
G
(S,G)
(S,G) Prune or
(S,G,rpt)

## Slide 27: Simple Multicast
Similar to CBT
  Draft-perlman-simple-multicast-03.txt (1999)
    1999, IETF March Meeting
  A multicast group is identified by (Core, G)
    A group = IP address of Core + Group address
    Class D address is not unique in the Internet
      Many Group addresses used by a Core
    No burden for Multicast address allocation
      MAAA (MALLOC WG)
  (Core,G) Join: from end host to Core
    Join_Request & Join_ACK
    Bi-directional tree like CBT

## Slide 28: Simple Multicast: Header Structure
IP header + SM header (Core, Group)

## Slide 29: Simple Multicast: Analysis
Benefits
  No Bootstrap of CBT
  Simple “Multicast Address Allocation”
Concerns
  Data Packet Format (for data transmission)
    (Source, Group, Core) Addresses
    Additional SM header
      For IP address of Core Router
      Existing: (Source, Destination = Class D)

## Slide 30: Source Specific Multicast
SSM History
  EXPRESS multicast:SIGCOMM’99
  Internet Drafts (March, 2000)
    SSM overview: draft-holbrook-ssm-00.txt
    SSM at Cisco
      draft-sandick-pimsm-ssmrules-00.txt
    SSM at Nortel: draft-bhaskar-pim-ss-00.txt
    Deployment at Sprint
      draft-bhattach-diot-pimso-00.txt
  Multicast Channel: (S,G)
    S: Unicast address of Source
    G: Class D Group address
  SSM is favored by ISPs (Scott Bradner)

## Slide 31: SSM: Motivation
Motivations
  PIM-SM: real SPT threshold (data rate) = “0”
  Most of multicast applications are one-to-many
  ISP wants tight control and management in MRP
    Easy traffic control of multicast source
    Effective billing and Management by (S,G) state

## Slide 32: SSM: Mechanism
Similar to PIM-SM
Join to Source, not RP
  Receiver => Router: IGMPv3 (S,G)
  Router => Source: SSM Join (S,G)
Subnet
R
R
Router
Source
SSM Join(S,G)
IGMPv3(S,G)

## Slide 33: SSM: Feature
Very Simple to implement and Manage
  Multicast Channel: (S,G)
    S: Unicast address of Source
    G: Class D Group address
    SSM(G) address
      232/8 (232.0.0.0 - 232.255.255.255)
  Requirements
    IGMPv3
      IGMP(S,G) query & report (SSM & PIM-SM)
    Forwarding Cache at Router
      by (S,G) state
    Source IP address
      Must be known to Receivers

## Slide 34: SSM: Example
S
G
G
G
Join (S,G)

## Slide 35: SSM: Analysis
Benefits
  Explicit Join to Source: like CBT, PIM-SM
    No Bootstrap mechanism (RP broadcasting)
  Using unicast routing table: by Join(S,G)
    No multicast routing tables (DVMRP, MOSPF)
  Simple multicast address allocation (No MAAA)
    G is not necessary to be “unique”
      Like Simple Multicast
  No Core us used : No SM header
Concerns (?)
  No support of shared tree (real concern ?)

## Slide 36: Summary
V3
V3 or other
V1/V2
IGMP
(S,G)
(Core, G)
MAAA or GLOP
Multicast Address Allocation
No change
Change
No change
Packet Format
Explicit Join
Explicit Join
Data-driven, Explicit Join
Join Mechanism (Bootstrap)
Unicast
Unicast
Multicast, Unicast
Routing Table Used
S,G
Core, G
G
Multicast Channel Identification
SBT
CBT(shared)
SBT/CBT(shared)
Tree Type
SSM
SM
ISM
Items

## Slide 37: QoS-based Multicast (1)
QoS Metrics in the viewpoint of Routing
  Tree Link Cost
    Scare Link Capacity Resource
    Cost of Transmission per Unit Bandwidth
  Delay
    From the Source
    Delay-sensitive applications
  Available Link Capacity
    For the required bandwidth
    Candidate Path with available link capacity

## Slide 38: QoS-based Multicast (2)
Some Example Studies
  QoSMIC: Quality of Service sensitive Multicast Internet protoCol”
    ACM SIGCOMM ‘98, September 1998.
  “DDMC: Destination driven routing for low cost multicast,”
    IEEE JSAC Vol. 15, No. 3, April 1997.
  “QDMR: an efficient QoS dependent multicast routing algorithm”,
    Proceeding of 5th IEEE real-time technology and application symposium (RTAS ’99)
  Non-core Based Shared Tree for IP Multicasting
    IEE Electronics Letters, pp. 872-873, Vol. 35, No. 11, May, 1999.

## Slide 39: Possible Approaches & Analysis (1)
SPT: for one-to-many
  Lowest Delay
  Tree cost may be high
Core Based Shared Tree: many-to-many
  Practical,but not optimized
Steiner Tree: NP-complete
  A minimum-cost tree spanning all group members
    Group Membership is Given (?)
    Membership Dynamics : Join & Leave
Delay-constrained Shared Tree
    Different metrics in application & Network
    Delay is source-specific
    In Shared Tree with multiple senders (?)

## Slide 40: Possible Approaches & Analysis (2)
Available Link Capacity : QoSMIC
  Candidate Path with available link capacity
  Select one of the candidate paths
  Network Topology Information is given ?
    Node & Link topology
    Link Transmission Delay
    Node Processing Power
    Available Link Capacity
QoS-based Approach
  Unicasting & Multicasting
  Theoretical or Practical ?
  Combined with the Internet QoS technology
    MPLS, RSVP/Intserv, Diffserv, VPN