## Slide 1: Reliable Multicast Transport
Seok Joo Koh

## Slide 2: Table of Contents
Review
RMT Overview
Existing Protocols
Currently Major Protocols in IETF RMT WG
IP Multicast Perspective

## Slide 3: IP Multicast Components
Multicast Application Services
  One-to-Many
  Many-to-Many
Session (Group) Management
  Session Creation
  Session Announcement: SDP/SAP, Web, E-mail
  Session Enrollment: Authentication
Multicast Routing & Forwarding
  Multicast Forwarding
Reliable Multicast Transport
  Reliability for Multicast Delivery
  QoS Requirements(?)

## Slide 4: Multicast Routing & Forwarding
IGMP: v1, v2, v3
Multicast Routing Protocols
  Internet Standard Multicast
    DVMRP/PIM-DM/MOSPF: Dense-Mode
    PIM-SM/CBT: Sparse-Mode
    MSDP/M-BGP/BGMP: Inter-Domain
  New Approaches
    SM
    SSM
    SGM
    ALM

## Slide 5: Reliable Multicast Transport (1)

## Slide 6: Reliable Multicast Transport (2)
RMT Issues (End-to-End Transport Issues)
  Error Control
    Reliable Data Transfer: Error-Free/Loss-Free
  Flow/Congestion Control
    Adjust the Data Transmission Rate
    Flow Control: Receiver side(Buffer)
    Congestion Control: network side
      Congestion Avoidance
  Security Issues
    Authentication
    Integrity

## Slide 7: Error Control or Recovery (1)
Components
  Error Types Corruption, Loss
  Functionality
    Error Detection
      by Receiver
    Retransmission Request
      From Receiver to Sender
    Retransmission
      Error Recovery

## Slide 8: Error Control or Recovery (2)
In TCP
  ACK(Acknowledgement)-based
Sender
Receiver
Cwnd=1
Cwnd=2
Cwnd=3
Cwnd=4
Data(1)
ACK for Data(1)

## Slide 9: TCP Header Format

## Slide 10: TCP Flow/Congestion Control
Window Size: ACK of Receiver
  Available (Receiver’s) Buffer Space
Sliding Window (in Sending Buffer)
  Three points: Start/Current/End
    End point = Start + cwnd
Congestion Avoidance
  Slow Start & Congestion Mode
    parameters: cwnd, ssthresh (RFC2001)
Start
Current
End
ACKed
Sent/UnACKed
To be sent

## Slide 11: Error Control in RMT
Scalability (many receivers)
  If TCP is applied to RMT
    ACK Implosions !!
    IF NACK, also NACK Implosions !!
Sender
Receiver
.. ..
Receiver
Receiver
Receiver
.. ..
ACK/NACK

## Slide 12: Many Approaches for RMT (1)
Classifications
  Reliability Mechanisms
    ACK or NACK based
  Repair Request and Retransmission
    Unicast or Multicast
  Feedback Control
    Structure or Timer based
  Flow Control
    Rate based or Window based
  Control
    Centralized or Distributed
  Group Management
    Explicit or Implicit

## Slide 13: Many Approaches for RMT (2)
General-Purpose Protocols
  RBP: Reliable Broadcast Protocol
  MTP: Multicast Transport Protocol
  RMP: Reliable Multicast Protocol
  XTP: Xpress Transport Protocol
  URGC: Uniform Reliable Group Communication
Multi-point Interactive Applications
  SRM: Scalable Reliable Multicast
  LBRM: Log-Based Receiver Reliable Multicast
  RAMP: Reliable Adaptive Multicast Protocol
  TRM: Transport Protocol for Reliable Multicast

## Slide 14: Many Approaches for RMT (3)
Data Dissemination Services
  Muse: multicast news on MBONE
  MDP: Multicast Dissemination Protocol
  AFDP: Adaptive File Dissemination Protocol
  TMTP: Tree-based Multicast Transport Protocol
  RMTP: Reliable Multicast Transport Protocol
  MFTP: Multicast File Transfer Protocol
Others
  STORM: Structure Oriented Resilient Multicast
  RMDP: Reliable Multicast Dissemination Protocol
  et al.

## Slide 15: Classification of Some RMT Protocols
Some of Existing RM Protocols
  RMTP: Tree based ACK (from child to parent)
  SRM: Multicast NACK
  PGM: Router Support
  MFTP: Specific to FTP (Round based)
  FEC: Forward Error Correction
  LGMP: Local Group based
See for more in detail
  http://research.ivv.nasa.gov/RMP/links.html
  http://www.nard.net/~tmont/rm-links.html

## Slide 16: Some Protocols (1)
SRM(Scalable Reliable Multicast)
  Sigcomm’95
  Receiver Initiated
  (Multicast) NACK based
    Retransmission Requests by using NACK
    NACK Suppression by Random Back-off Timer
    Multicast Retransmission
  http://www.aciri.org/floyd/srm.html
    SRM applications: wb, MediaBoard, …
    with ALF(Application Level Framing)
  NORM BB & PI: IETF RMT WG

## Slide 17: Some Protocols (2)
RMTP (Reliable Multicast Transport Protocol)

## Slide 18: Some Protocols (3)
PGM (Pretty Good Multicast)
  WhiteBarn => Talarian

## Slide 19: Some Protocols (4)
MFTP (Multicast File Transfer Protocol)

## Slide 20: Some Protocols (5)
LGMP (Local Group based Multicast Protocol)
  Mark Hofmann: www.telematik.informatik.uni-karlsruhe.de/~hofmann/

## Slide 21: Some Protocols (6)
FEC (Forward Error Correction)
  No Feedback
  For k Source packets, Transmit n packets
    n = k + (n - k)
    n - k : Redundancy
  FEC coding
    Simply, n = k + 1
    LT Code
    Tonado code
    etc..

## Slide 22: IETF RMT WG
IRTF RMRG (Reliable Multicast Research Group)
IETF RMT WG: 1999. 3
  Building Block Approach
  One-to-Many Bulk Data Transport
Three Major Protocol Instantiations (PIs)
  Tree based ACK (TRACK)
  NACK Oriented Reliable Multicast (NORM)
  Asynchronous Layered Coding (ALC)
Building Blocks
  Congestion Control
  Generic Router Assist
  Forward Error Correction (FEC)
  Tree Configuration, NACK BB, etc

## Slide 23: RMT WG Draft
General
  RMT BBs for One-to-Many Multicast
  RMT Design Space
  Author Guidelines for RMT BB and PI documents
BB
  Generic Router Assist (GRA)
  Multi-rate Congestion Control
  Forward Error Correction
  Tree Auto-Configuration
PI
  Asynchronous Layered Coding (ALC)
  TRACK PI Architecture
    Security Requirements For TRACK (?)

## Slide 24: TRACK (1)
Base Protocols
  RMTP-II: Talarian Corporation
  TRAM: Sun MicroSystems
  ECTP: ETRI (ITU-T SG7, JTC1/SC6)
RMTP-II
  RMTP (Lucent): 1994 – 1997 (Sanjoy Paul)
  RMTP-II Version 1 (Globalcast): 1997. 9.
  RMTP-II Version 2 (Talarian): 1999
  Implementation: on Windows NT 4.0 & Sun Solaris
  Extensional features (FEC, Congestion Control)
    Working on progress

## Slide 25: TRACK (2)
Talarian Corporation
  2000. 4. 13: IPO (Initial Public Offering)
  2000년 5월: Acquisition of WhiteBarn (PGM)
  Product Family
    Smart Socket
    Mqexpress (middle-ware)
    RMTP-II
    PGM
SUN MicroSystems
  Project: Java Reliable Multicast Services
    1998 -

## Slide 26: TRACK (3)
ETRI (ECTP)
  Joint Project of ITU-T SG7 & JTC1/SC6/WG7
    X.ectp | CD 14476.4 (under 4th ballot process)
  Main Contributions from Korean Experts
ECTP Features
  Multicast Transport Protocol running over IP
    IETF: RMT over UDP
In addition to IETF RMT, ECTP supports
  Connection (Session) Management
  End-to-end QoS negotiation/arbitration
  Many-to-many group communications

## Slide 27: FEC based ALC
Base Protocol
  RMDP, etc
Digital Fountain
  Venture Corporation (1998)
    Capital 7 millions $, 20 Employees
    CEO: Cliff Meltzer (IBM & Cisco 20 years)
    CTO (chief technical officer): Mike Luby
      UC Berkley
  FEC based error control
    Patent-pending Tech. + Mathematical algorithm
  ALC: Multi-rate based Congestion Control

## Slide 28: NORM
Base Protocol
  SRM (Scalable Reliable Multicast)
USA Universities
  Sally Floyd (ACIRI)
  MBONE: Whiteborad application
Status
  NORM BB: very rough (framework for RMT)
    Generic Overview of NACK and RM approach
  NACK suppression with exponential back-off timer

## Slide 29: TRACK PI
Leading Drafting Members
  Brian Whetton (Talarian)
  Dah Ming Chiu (Sun MicroSystem)
Related Drafts
  TRACK architecture
    Initial material by Brian Whetton (2000. 2)
    Reviewed by Dah Ming and et. al. (2000. 3 - 6)
    WG draft: 2000. 7
  Tree Configuration BB: 2000. 7
    Brian Levine, Brad Cain + TRAM + RMTP + ECTP
  TRACK Security: 2000. 7

## Slide 30: TRACK Architecture

## Slide 31: Packet Types
Tree Bind & Confirm Packet (Accept & Reject)
Data Packet
  Retransmission Data Pakcet
Null Data Packet
ACK Packet
  NACK: ACK with a flag of 1
Leave Request & Confirm Packet
Heartbeat Packet
  Heartbeat Response Packet
Eject Packet (for troublemaker)

## Slide 32: Tree Configuration BB
History
  2000. 1 : RMT WG Interim meeting
  2000. 3 : IETF meeting (Adelaide) Issues
    No ERS & Many-Many Multicast (TRAM)
    No Dedicated Server for Repair Heads (RMTP)
  2000. 7 : RMT-TREE group meeting
  2000. 8 : IETF meeting (Pittsburg)
    Drafts are submitted (a rough sketch still)

## Slide 33: Tree Configuration: Overview
Control Tree
  A path for control Packets
  ACK: from Children to Parent
  Retransmission: From Parent to Children
Bottom-Up
  Receiver-Initiated
    Each receiver learns the Distance from Sender
    How ?: Four Metrics
  Open Group/Loose Control in Internet Environment
  No Connection Management Concept !
  No Loop Guarantee ?

## Slide 34: Tree Configuration: Issues
No Loop Guarantee ?
  Bottom-Up approach
Consistent with four metric ?
  Example) Heartbeat message
    ERS (from parent to child)
    GRA (from a child to parent)
Depend on TTL and Many-to-Many multicasting
  ERS
Top-Down Configuration (in ECTP) ?

## Slide 35: IP Multicast: Current
Multicast Routing
  Existing: DVMRP/MOSPF/PIM/CBT/MSDP/BGMP
  New: SSM(IGMPv3), SGM, SM
Difficulty
  Inter-Domain Multicast Routing
    Negotiation and Policy between ISPs
  Traffic Control & Management
    Membership (Sender/Receivers) Management
    Billing/Charging/Authentication
Application Level Multicasting
  Mixed with Unicast
  Application Relays: Multicast Hosting

## Slide 36: IP Multicast: Tomorrow
IP Multicast or Application Relays
  Mixed Solutions: ALM (?)
    Unicast in Backbone & Local Multicast (SSM)
IP Multicast Deployment Depends on
  When ? : 1 - 3 or 5 - 10 years, or other tech. ?
  Killer Applications
    Internet TV Broadcasting
    Real-Time & Unreliable
  Multicast Business Model
    Does IP Multicast make money (How many users)?
    Initial Investment Cost (Router/Software)