## Slide 1: Inter-Domain Multicast Routing Protocols
Seok Joo Koh

## Slide 2: Table of Contents
Review
Inter-Domain Multicast Routing Overview
MSDP/PIM-SM
Multicast Address Allocation Architecture
BGMP/MASC
Advanced Topics
  Small Group Multicast
  Application Level Multicast

## Slide 3: Source Specific Multicast (SSM)
One Promising Solution for MRP
Benefits
  Explicit Join to Source: like CBT, PIM-SM
    No Bootstrap mechanism (RP broadcasting)
  Using unicast routing table: by Join(S,G)
    No multicast routing tables (DVMRP, MOSPF)
  Simple multicast address allocation (No MAAA)
    G is not necessary to be “unique”
      Like Simple Multicast
  No Core us used : No SM header
Concerns (?)
  No support of shared tree (real concern ?)

## Slide 4: Summary of Intra-Domain MRP
V3
V3 or other
V1/V2
IGMP
(S,G)
(Core, G)
MAAA or GLOP
Multicast Address Allocation
No change
Change
No change
Packet Format
Explicit Join
Explicit Join
Data-driven, Explicit Join
Join Mechanism (Bootstrap)
Unicast
Unicast
Multicast, Unicast
Routing Table Used
S,G
Core, G
G
Multicast Channel Identification
SBT
CBT(shared)
SBT/CBT(shared)
Tree Type
SSM
SM
ISM
Items

## Slide 5: Inter-Domain Multicast Routing
Issues
  Domain-Specific Multicast Routing Policy
    Domain: Region, AS(Autonomous System) or ISP
  Multicast Source Discovery: MSDP WG
    Where is the Group Source?
    Discovery of Sources in different domains
  Multicast Address Collisions: MALLOC WG
    Efficient Address allocation in Global Internet
  Multicast Routing between Domains: BGMP WG
    Tree of Domains
Solutions (?)
  MSDP/PIM-SM: near-term
  BGMP: long-term (?)

## Slide 6: MSDP: Background
Multicast Source Discovery Protocol
  draft-ietf-msdp-spec-06.txt (July 2000)
BGMP
  Long-Term Solution
    Need Near Term Solution
  Near Term Approach
    To connect existing shared trees
MSDP
  No inter-domain shared trees
  Just inter-domain source trees
  Reduces to problem of locating active sources
  RP joins inter-domain source tree

## Slide 7: MSDP: Overview
MSDP/PIM-SM
PIM-SM
  In a domain
  RP <-> Receivers
MSDP
  Between RPs in different domains
    RP <-> RP: TCP connection
  To Discover a source in a different domain
  If the source is found,
    Source - RP
    Shortest Path Tree

## Slide 8: MSDP: Mechanism
MSDP Peering Session (Pre-configured)
  Between RPs in different domains
  By using M-BGP(BGP4+)
    Exchange of Information on RP in the Domains
  Runs over TCP
  Inter-Domain RP Topology
SA (Source Active) messages
  (S,G) Information
  Flooding to the other MSDP-peer RPs
SPT Configuration
  SPT between RP and Source
  RP sends a (S,G)-join to the Source

## Slide 9: MSDP: Example (1)
MSDP Peering between RPs (via TCP)
RP2
Receiver R
RP1
Source S
MSDP Peering

## Slide 10: MSDP: Example (2)
Source S is known to the Receivers
RP2
Receiver R
(S,G)
Join
towards
RP2
AS 2
RP1
Source S
Source sends (S,G)
Register to RP1
RP1 creates
state
AS 1

## Slide 11: MSDP: Example (3)
Source Active (SA) message: (S,G)
  Distributed to all RPs (over MSDP peering)
RP2
Receiver R
RP1
Source S
(S,G) Join toward RP2
MSDP Peering
RP1 sends (S,G) SA message

## Slide 12: MSDP: Example (4)
RP2 sends (S,G) Join to Source (Not RP1)
RP2
Receiver R
RP1
Source S
MSDP Peering
(S,G) Join
RP2 joins (S,G) Source Tree

## Slide 13: MSDP: Example (5)
SPT from Source S to RP2
  Another RP3 may be involved in the SPT
RP2
Receiver R
RP1
Source S
MSDP Peering
Data
SPT

## Slide 14: MSDP: Analysis
Features
  Connect multiple PIM-SM domains together
  Each PIM-SM domain uses it’s own independent RP(s)
  Do not depend on RPs in other domains
  Not connecting trees,
    Connect sources known to all trees
Benefits
  PIM-SM domains rely on their own RPs only.
  Domains with only receivers get data
    without globally advertising group membership.
  Global source state is not required.

## Slide 15: MSDP: Summary
MSDP/M-BGP/PIM-SM
  Flood-and-Join mechanism
    Flooding of SA to all MSDP-peering RPs
    Join from RP to Source
  Simple to implement
    Near-term solution
    Being implemented and deployed
  Scalability
    Many Sources => many SA flooding !!
  Large Latency to Receive Data
    by Periodic SA messages and then (S,g) Join
    Bursty source with short lifetime
      Not effective !

## Slide 16: Multicast Address Allocation
Issues
  Address Collision
    A Group address may be used by several sessions
    More Group addresses, More severe Problem !1
  How should Group Addresses be assigned ?
    For Senders or Group Sessions
    Without Collisions, and Systematically
Need to Standardize the address allocation
  MALLOC (Multicast Address Allocation) WG
  Multicast Address Allocation Architecture (MAAA)
    Dynamic and Hierarchical address allocation
    Easy & Effective ?

## Slide 17: Multicast Address Collision
  Today’s Router Memory: 2,000 group addresses
  Total address space: 2^28 (Random Allocation)
  More addresses, More Collisions !!

## Slide 18: Four Possible Approaches
MAAA
  Multicast Address Allocation Architecture
  IETF MALLOC WG
GLOP (Static Allocation and Assignment)
  GLOP addressing in 233/8 : RFC2770 (Feb., 2000)
New Routing Protocols
  Simple Multicast : (Core, G) channel
  Source Specific Multicast (SSM): (S,G) channel
    G can be assigned to each Core or S !!
Multicast in IPv6
  120 bits : multicast address space

## Slide 19: MAAA
Multicast Address Allocation Architecture
  MALLOC WG: RFC2908 (September 2000)
Three Protocols defined in MAAA
  MADCAP (RFC 2730)
    Multicast Address Dynamic Client Allocation P.
    Hosts request addresses from (MAAS) servers
  AAP (draft-ietf-malloc-aap-04.txt)
    Address Allocation Protocol
    Servers inform each other of claimed addresses
  MASC (RFC 2909)
    Multicast Address Set Claim protocol
    Allocation of addresses between domains

## Slide 20: MAAA: Intra-Domain Protocol (1)
MAAS
Client
Client
MAAS
Client
Client
MAAS
Client
Client
Prefix
Coordinator
Prefix
Coordinator
Layer 1
Layer 2

## Slide 21: MAAA: Intra-Domain Protocol (2)
Within a Domain
Layer 1
  Between a Client to MAAS
    MAAS: Multicast Address Allocation Server
  Possible Method
    MADCAP : RFC2908
    HTTP: Web Page for Allocation
    IANA Static Address allocation
Layer 2
  Between MAAS and Prefix Coordinator
  AAP: Internet Draft

## Slide 22: MAAA: Inter-Domain Protocol
Layer 3: Between Domains
  MASC: RFC2909
  Exchange of Prefix Coordinator Information
Prefix
Coordinator
Prefix
Coordinator
Layer 3
Prefix
Coordinator
Prefix
Coordinator

## Slide 23: GLOP Addressing in 233/8
Static Allocation and Assignment
  IETF MboneD WG
    RFC 2770 (Feb., 2000)
    GLOP uses Autonomous System (AS) numbers
      (e.g) AS 5662: 233.22.30/24
    Experiments will be reviewed in May 2000
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 233 | 16 bits AS | local bits |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 24: Summary of Address Allocation
MAAA: Dynamic allocation of addresses
    Efficient use of address space
      MAAA: Hierarchical Prefix
    At the cost of complex design
GLOP: Static Assignment
  Based on the AS number
    Starvation of addresses
Multicast Group Channel
  Simple Multicast: Core (IP address) + G
  SSM: Source (IP address) + G
    Freely Use in Core or Source
IPv6
  Large Space for Address Allocation (120 bits)

## Slide 25: BGMP/MASC: Overview
Inter-Domain Multicast Routing
  Near-term solution: MSDP/PIM-SM
    SPT between RP and Source
  Long-Term: BGMP/MASC
    Bi-directional Shared Tree of Domains
MGMP/MASC
  MASC(Multicast Address Set Claim) Protocol
    Hierarchical allocation of multicast addresses
  BGMP(Border Gateway Multicast Protocol)
    Bi-directional Shared Tree of Domains
      Root Domain <=> Core/RP
    Selection of the Root Domain with MASC Protocol

## Slide 26: MASC
Domain A
224.0.0.0/16
Domain C
224.0.1.1/25
Domain F
Domain G
Domain D
Domain E
A1
A2
A3
A4
B1
B2
F1
D1
E1
C1
C2
G1
Domain B
224.0.128.0/24
Address Allocation among Domains

## Slide 27: MASC: Mechanism
Distribution of Address Information via BGP
  B1 advertises the group address by prefix
    224.0.128.0/24 to A3 via BGP
    The address is stored by A3
      as (224.0.128.0/24, B1)
    B1 is the next hop from A3
    A1, A2, A4 also store (224.0.128.0/24, A3)
Aggregation
  Address Range allocated to A: 224.0.0.0/16
    A subsumes B’s address
  A’s border routers need not propagate 224.0.128.0/24 to the other domains

## Slide 28: BGMP: Overview
Like CBT & PIM-SM
  Root Domain = Core/RP
  Bi-directional Tree: CBT
  Source-Specific Branch: PIM-SM
Bi-directional Shared Tree of Domains
  BGMP builds bi-directional group-shared tree
Source-specific Branch by a Domain
  If the shortest path to a source does not coincide with the bi-directional tree from the domain
Root of the Shared Tree
  Inter-domain : by MASC (Group Address Prefix)
  Intra-domain : typically by hashing function

## Slide 29: BGMP: Shared Tree of Domains (1)
Domain A
Domain B
224.0.128.0/24
Domain C
Domain F
Domain G
Domain D
Domain E
A1
A2
A3
A4
B1
B2
F2
D1
E1
C1
C2
G2
Domain H
H1
G1
H2
Data
Bi-directional
BGMP Forwarding
Root domain
for 224.0.128.1
F1

## Slide 30: BGMP: Shared Tree of Domains (2)
Establish a Bi-directional Shared Tree
  A group is created by a host in domain B (224.0.128.1)
  When a host in domain C now joins this group, a join request is received from the MIGP by the BGMP of C1
  C1 finds (224.0.0.0/16, A2) in G-RIB, and creates a forwarding entry (*, G) with target list (A2, MIGP)
  After creating the (*, G) for 224.0.128.1, C1 sends a group join message A2
  A2 finds (224.0.128.0/24, A3) in G-RIB, and then establishes a (*, G) with (A3, C1)
  A2 transmits the join request to its MIGP (A2->A3)
  A3 finds (224.0.128.0/24, B1) in G-RIB, creates a (*, G) with (B1, A2)
  B1 is a root domain, so creates a (*, G) entry with (MIGP, A3)

## Slide 31: BGMP: Source-Specific Branch (1)
Domain A
Domain B
224.0.128.0/24
Domain C
Domain F
Domain G
Domain D
Domain E
A1
A2
A3
A4
B1
B2
F2
D1
E1
C1
C2
G2
Domain H
H1
G1
H2
Data
Bi-directional
BGMP Forwarding
Root domain
for 224.0.128.1
F1
S
Source-specific
Branch

## Slide 32: BGMP: Source-Specific Branch (2)
Establish the Source-specific Tree from F
  There are members in domains B, C, D, F and H
  Domain F has an Inter-domain link to domain A via F2
  Since only F1 is on bi-directional shared tree, data from a source S domain S will be received by F1
  F1 must then encapsulate the data packets to F2
  F2 injects the data into the its domains
  F2 may send a source-specific join towards S, also makes a multicast forwarding entry (S, G): (A4, MIGP)
  Source-specific join from F propagates toward S setting up (S, G)
  Subsequent data packets sent by S and received by A4 are forwarded to all other targets in (S, G) including F2

## Slide 33: BGMP: Related Works
HPIM: Hierarchical Protocol Independent Protocol)
  M, Handley, J. Crowcroft, et, al
  Builds on PIM-SM by using a hierarchy of RPs for a group
OCBT: Ordered CBT Protocol
  C. Shield, et, al, Infocomm’97
  Extension of CBT where a hierarchy of cores is used
HDVMRP: Hierarchical DVMRP for MBONE
  S. Deering, et, al, (ACM SIGCOMM’95)
  Interconnects regions(domains) running any of the existing multicast protocols

## Slide 34: Summary: Internet Standard Multicast

## Slide 35: Small Group Multicast (SGM)
Motivation
  Current Multicast Schemes
    are not “Generally” available
    Not Support Certain applications very well
      IP Telepony with Conferencing
      Video-Conferencing, Real-time Collaborative
    Contains
      State Information
      Signaling
      Administrative Complexity
Status
  Initiated by Internet2
  IETF BOF: 2000. 7

## Slide 36: SGM: Features
Support “Small Groups”
  as in IP telephony & Conferencing
  Large Number of Small Groups
No multicast Routing Protocol/Signaling
No stored state on Routers
No need to exchange Routing Information
Eliminate Difficulty of MRP
  Administrative Complexity
  Difficult conversation between ISPs

## Slide 37: SGM: Overview

## Slide 38: SGM: Analysis
Cons
  Extra Bytes in IP Packet Header
  New Stack for packet processing
  Not Suitable for larger broadcast-like multicast
Pros
  Scalable to Large network
  No per-flow state information
  No routing protocol
  No Class D address
  Extra Bytes in IP Packet Header

## Slide 39: SGM: Transition Plan
Based on SGM Backbone
  Initially, based on several SGM-capable routers

## Slide 40: ALM
Motivation
  Deployment of IP Multicast is Slow
    In particular, in WAN (Core/Backbone Network)
  Many Application requires Multicast Delivery
Delivery Scheme
  Unicast: Sender to Local Multicast Regions
  Multicast: Within the Multicast Regions
    Unicast, if multicast is not supported
  Unicast in WAN, and Multicast in LAN
Pre-configuration of Unicast WAN
  Tree or Mesh between Regions

## Slide 41: ALM: Example

## Slide 42: ALM: Related Projects
IMA: Internet Multicast Architecture
  France, INT (Research Institute)
YOID: Your Own Internet Distribution)
  http://www.aciri.org/yoid/
    YOID Tree Management Protocol
    YOID Distribution Protocol, etc
End System Multicast
  CMU School of Computer Science
RMX: Reliable Multicast proXies
  UC Berkeley Computer Science