## Slide 1: Multicast Routing Protocols in Dense Mode
<Chapters 7 - 10 in Textbook>
Seok Joo Koh

## Slide 2: Table of Contents
Review
Reverse Path Multicasting
Distance Vector MRP
Protocol Independent Multicast - Dense Mode
Multicast extensions to OSPF

## Slide 3: Internet Communications
Encapsulation
Application
IP
Data Link
Physical
TCP/UDP
Application
IP
Data Link
Physical
TCP/UDP
IP
Data Link
Physical
IP
Data Link
Physical
Decapsulation

## Slide 4: Encapsulation
Application (Data Stream)
TCP or UDP Header
IP Header
Ethernet (MAC) Frame header
Physical Layer: SONET/SDH
  Optical bit (0/1) transmissions
Ethernet
IP
TCP/UDP
Application Data

## Slide 5: Protocol Layer
Examples
  IGMP, Routing Protocols over IP
  MSDP(Multicast Source Discovery Protocol)over TCP
  Reliable Multicast Transport Protocol over UDP
IP
Data Link
Physical
IP
Data Link
Physical
UDP
IP
Data Link
Physical
TCP
IGMP
MSDP
RMTP

## Slide 6: IGMP
IGMPv1: Query & Report(G)
IGMPv2: Lower Leave Latencey
  Leave Group(G) & Group-Specific Query(G)
IGMPv3 (S,G): Source Filtering

## Slide 7: Classification of MRP
Tree Types
  Source-Specific Tree
  Center-based Shared Tree
Join Types
  Data Driven (Implicit Join)
  Explicit Join

## Slide 8: Multicast Routing Protocols

## Slide 9: Reverse Path Multicasting
Flooding: naive broadcasting
RPB (Reverse Path Broadcasting)
  Flooding + Reverse Path
    Reverse Path Forwarding
  Reverse Path: shortest path toward Source
TRPB (Truncated RPB)
  RPB + Truncated (Based on IGMP)
    Stop forwarding to Subnet
RPM
  TRPB + Prune + Grating
  Prune the branch from the tree, if no member
  Grafting, if a member appears again

## Slide 10: Flooding
Naive Broadcasting
S
R
R
R

## Slide 11: RPB
First, Dalal and Metcalfe (1978)
Operations
  Reverse Path: shortest path toward Source
    In terms of the local router
    Parent link & Child links
  If a packet arrives on the parent link, the router forwards the packet on all the child links
    Otherwise, discard the packets
  Routing Table
    keeps the information on parent and child links
    Exchanges Routing Tables with Neighbor Routers

## Slide 12: Reverse Path Broadcasting
Reverse Path (by Multicast Routing Table)
S
R
R
Parent Link
Child Link
R
R

## Slide 13: Reverse Path
Unicast (Path)
  Based on Destination Address
  Where to send the packet toward ?
Multicast (Reverse Path)
  Based on Group (Destination) Address
  Where to receive the packet from ?
Unicast
Multicast
To where to send ?
From where to receive ?

## Slide 14: Truncated RPB
RPB + Truncated (based on IGMP)
S(G1)
Active Branch
Inactive Branch
G1
G1
G1
G2
group member G1

## Slide 15: Reverse Path Multicasting
Enhancement to RPB and TRPB
  Delivery Tree includes only
    Subnetworks with Group members
    Along the shortest path from Source to Receivers
Truncated RPB + Prune + Graft
  Prune
    If no member in the subnet and downstream
    Periodically
      Upstream routers keep the Prune State
  Grafting
    If a member appears again
    Router forward Grafting message toward Source

## Slide 16: Prune
Periodic Prune message to Upstream Routers
S
Prune Message
R
R
Prune Message

## Slide 17: Grafting
Grafting Prune message to Upstream Routers
  Until active delivery tree is reached
R
S
Graft Message
R
Graft Message
R
R

## Slide 18: RPM: Limitations
Improvement to TRPB, but ..
Scalability
  Multicast packets must periodically be broadcast across every router in the network
    Wasteful of Bandwidth
  Every router must have forwarding table entries and Prune State information for each (S,G) pair
    for large group and many sources
Used by DVMRP and PIM-DM
Induces Shared Tree approach

## Slide 19: DVMRP
Distance Vector Multicast Routing Protocol
  First defined in RFC 1075 (1988)
  Derived from RIP and TRPB
    Routing Information Protocol : RFC 1058
  Major difference between RIP and DVMRP
    RIP: next hop toward destination
    DVMRP: previous hop back toward Source
  Currently, DVMRP version 3 (IDMR WG draft)
  Still employed in MBONE
    Since mrouted 3.0, DVMRP use RPM
  DVMRP implements the RPM algorithm

## Slide 20: Note: RIP for Unicast
RIP (Routing Information Protocol)
  The First Dynamic Routing Protocol in Internet
  Distance Vector protocol
    Exchange Routing Tables with Neighbors
    Bellman-Ford Algorithm for Shortest Path
  Small network within 15 hops (Restricted)
  Classful Routing: Not subnetting, Not CIDR
    Inefficiency in Networks with many Sunets
    Induces the RIP version 2
  Slow adaptation to topology change
  DVMRP is based on RIP
    in terms of DVMRP routing table updates

## Slide 21: Note: OSPF for Unicast
OSPF (Open Shortest Path First)
  Link State Protocol
    Flooding Routing Tables (LSA) into the Domain
    Dijkstra Algorithm for Shortest Path
  Suitable for QoS routing
    LSA (Link State Advertisements)
    Cost, Bandwidth, Distance, ...
  Within an AS (Autonomous System) domain
  Classless Routing & Subnetting
  Interaction with Exterior Gateway Protocol (BGP)
    Exterior : BGP
    Interior : OSPF
  MOSPF is based on OSPF

## Slide 22: Unicast Routing Protocols
Distance Vector: Interaction with Neighbors
Link State Protocol: Flooding into the Domain
  Realize Topology Information !
Distance Vector
Link State

## Slide 23: Note
Unicast Routing Protocols
  Static (Configured) Routing
  RIP (Routing Information Protocol)
    RIPv1, RIPv2
  OSPF (Open Shortest Path First)
  IS-IS: From ISO/IEC JTC 1
    Intermediate System to Intermediate System
  (Interior) BGP
  ...

## Slide 24: DVMRP: Operations (1)
Based on the DVMRP Routing Table
  Contain Reverse Path information
The first datagram is broadcast
  Not all non-incoming, but downstream links
    by “Poison-Reverse” (in routing table update)
  Forwarding Table is created
Prune Process
  Inactive branch is removed
    From leaf routers
Grafting Process
  Active branch is re-created

## Slide 25: DVMRP: Operations (2)
Based on DVMRP routing table at each router
S
Prune or Graft
R
Prune or Graft
R
R

## Slide 26: DVMRP: Routing Table
Periodic exchange and update of Routing Table
Based on the Routing table
  Create Forwarding table
Not contain Group membership & Prune

## Slide 27: DVMRP: Forwarding Table
Based on DVMRP Routing table
Group membership & Prune
Input/Output Interfaces for Multicast Packets

## Slide 28: DVMRP: Weakness
Slow to adapt to topology change
  Slow to converge
Limited network diameter (15 hops)
Maintain source-specific state when not on-tree
  Waste Router memory
  Not scale for larger number of sources
Scalability
  Multicast traffic is periodically broadcast across the entire network

## Slide 29: PIM-DM
Protocol Independent Multicast
  Independent of Underlying Unicast Protocol
  It needs any one unicast routing protocol
    DVMRP: DVMRP multicast protocol
PIM
  Sparse Mode: Sparsely distributed
  Dense Mode: Densely distributed
PIM-DM is based on RPM algorithm
  Like DVMRP
  broadcast
  prune
  graft

## Slide 30: PIM-DM vs. DVMRP
Broadcasting
  DVMRP: only child interfaces
  PIM-DM: all non-incoming interfaces
    Until explicit Prune messages are received
    Because no distinct MRP
  Tradeoff
    duplicated packets vs. simple mechanism
Reverse Path Check
  DVMRP: Reverse Path calculation by Routing table
  PIM-DM: Depends on Unicast Routing Table
    Considers Multicast Source as Desination
    Previous Hop Calculation

## Slide 31: Broadcasting: PIM-DM vs. DVMRP
DVRMP: Only child interfaces
PIM-DM: all non-incoming interfaces
Router
DVMRP
Router
PIM-DM

## Slide 32: MOSPF (1)
Open Shortest Path First
  OSPF Version 2: RFC 2178
  OSPF is an Interior Gateway Protocol (IGP)
    distributes unicast topology information
    among routers belonging to a single OSPF AS
  Routing Table calculation: Link State algorithm
    Rapid & efficient Route calculation
    at the cost of Routing Protocol Traffic
  Link State Advertisement (LSA)
    Link Cost, Available bandwidth, length, etc..
  Hierarchical routing, load balancing, etc.

## Slide 33: MOSPF (2)
Multicast extensions to OSPF
  RFC 1584
  MOSPF routers maintain a current image of the network topology via unicast OSPF protocol
  MOSPF are built on top of OSPFv2
  MOSPF Routers inter-operate with non-MOPSF routers
    when forwarding unicast IP data traffic
Intra-Area routing with OSPF
  source and destination are all in a single area
Inter-Area routing with OSPF
  source or some receivers are in a different area

## Slide 34: Local Group Database
LSA (Link State Advertisement)
  OSPF database: LSA (with topology information)
Group-Membership LSA
  MOSPF (with help of IGMP)
  MOSPF database: LSA + Group membership LSA
MOSPF routers maintain
  LSA and Group-Membership
  into LSA its local database
MOSPF router
  communicates group membership information to all other routers in the OSPF area
  by flooding “Group-Membership LSA”

## Slide 35: OSPF: Shortest Path Tree
Shortest Path Tree
  Path From source to receivers for a (S,G) pair
  Built “On Demand”
    when a router receives the first multicast packet for (S,G) pair
  calculated based on
    OSPF LSA (topology)
    MOSPF Group-membership LSA (by IGMP)
      Location of group members are known !!
      Delivery tree spans only the routers with the group embers !!
    Not RPF (Reverse Path Check, DVMRP)
  Dijkstra’s algorithm

## Slide 36: OSPF: Operations
S
R
For all MOSPF router,
- LSA + Group-Membership LSA
- “On-Demand” Tree Calculation
=> Forwarding Cache
R
R
R

## Slide 37: Forwarding Cache
Built from the shortest path tree for (S,G)
  When the first data arrives (On-demand)
  Forward all subsequent data from UP to DOWN
All MOSPF routers have the same SPT information
  Forwarding cache is created
    according to its location along the SPT tree

## Slide 38: MOSPF: Summary
Source-rooted Shortest Path Tree
  as DVMRP, PIM-DM
Explicit Join
  Tree can be calculated
    After IGMP information is sent to Source Subnet
    via Group-Membership LSA
Data-Driven
  After the first data arrives, the tree is now calculated (with forwarding cache)
Interoperable with unicast OSPF

## Slide 39: MOSPF: Weakness
Dijkstra’s algorithm must be run
  every time a new (S,G) pair is seen
  Waste CPU resource
LSA (with Group Membership) flooding
  to identify network topology and group information
    as OSPF
  Too much control overhead
Not scalable to large network and group !

## Slide 40: Summary
Dense Mode
  most of group members are densely distributed
    Within a small network
Multicast Routing Protocols
  DVMRP
  PIM-DM
  MOSPF
Not scalable to large network or Sparse Group
  but, deployable in the small intranet
    Requires abundant network resources
    Small number of Sources and Groups